## Slide 1
Tuning Space Mapping: The State of the Art
Q.S. Cheng, J.W. Bandler, and S. Koziel
Simulation Optimization Systems Research Laboratory McMaster University, www.sos.mcmaster.ca, chengq@mcmaster.ca
Bandler Corporation, www.bandler.com, john@bandler.com Engineering Optimization & Modeling Center, Reykjavik University, koziel@ru.is
presented at
Third International Workshop on Surrogate Modelling and Space Mapping for Engineering Optimization (SMSMEO 2012)
August 9-12, 2012, Reykjavik University, Iceland
Notes: 1
Good morning everybody, today I will present
This work is in collaboration with Dr. Slawomir Koziel

## Slide 2
Tuning Space Mapping Approach
simultaneously achieves electromagnetics (EM) accuracy and circuit-design speed
based on the intuitive idea of “space mapping” and an EM-simulator-based tuning methodology
we review the state of the art of computer-based optimal tuning of microwave circuits
we explain the art of microwave design optimization through our “tuning space mapping” procedures
Notes: In today’s preseantation, I will discuss
Tuning sm is trying to achieve high accuracy and fast design
TSM is based on the …. As dr. bandler has discussed in the previous presentation. Also based on em which we will discuss

## Slide 3
Tuning Space Mapping Procedures
involve three models
fine model
auxiliary fine model (fine model with tuning ports) of various distinct types (e.g., Type 1 and Type 0)
tuning models (auxiliary fine models augmented with
tunable or tuning elements)
we implement these models utilizing commercial simulation software
1
2
3
Notes: Surrogate-based technique such as space mapping is much faster than the traditional gradient-based method.

## Slide 4: Postproduction Tuning computer-aided network tuning (Pinel, 1971) design centering, tolerancing and tuning (Bandler et al., 1976) postproduction tuning technique utilizing simulated sensitivities and response measurements (Bandler et al., 1981) functional and integrated tuning approach (Bandler and Salama, 1983, 1985) a scalar transmission-based tuning technique (Zahirovic et al., 2010) tuning robot (Yu and Tang, 2003)
Notes: Postproduction tuninig is a procedure to adjust certain parameters of a device after it was built in order to satisfy certain specs.
In 1971 Pinel proposed a ….. Which discuss a design procedure for a device that requires the postproduction tuning.
Dr. Bandler and his colleagues, proposed more advanced procedures for tunable devices.
Worth of mentioning is Dr. Ming yu of Comdev, Canada, who is here with us in this workshop developed an interesting tuning robot which can tune a filter automatically.

## Slide 5: Electromagnetics-Simulator-Based Tuning fast analysis and optimization of combline filters using tunable components in FEM simulator (Swanson and Wenzel, 2001) design closure—companion modeling and tuning methods (Rautio, 2006)
Notes: Now let’s turn to EM simulator based tuning. In 2001 Swanson and his colleagues implemeted fast analysis and optimization of a combline filter using used tuning elements in an FEM simulator to perform tuning.
Dr. Rautio of Sonnet Software, discussed companion model and tuning method that implemented similar tuning idea in Sonnet software.

## Slide 6
Space Mapping Concept (Bandler et al., 1994-)
Notes: How does the tuning relate to SM? Space mapping was pioneered by Dr. John Bandler and his colleagues in 1994. The basic concept is that we have a fine model, normally a model based on full wave EM simulation. It is accurate but usually cpu intensive. We also have here a coarse model. It is a physics based model, such as circuit model, it is fast but not as accurate as a fine model. Space mapping adds a mapping to the coarse model. The mapping and coarse model together is our surrogate model. By changing the parameters of the mapping we could match the responses of the surrogate to the responses of the fine model. The surrogate can now be used for modeling purpose or design purpose.

## Slide 7
Implicit, Input and Output Space Mappings (Bandler et al., 2003-)
expert engineering expertise helpful in engineering expertise
knowledge helpful “tuning the surrogate” perhaps less necessary
(few designable (many possibilities, (many output variables)
variables) e.g., dielectric constant)
Notes: Recent years space mapping has been expanded to include many variations. Here I show a comprehensive space mapping framework that contains input space mapping, implicit space mapping and output space mapping. input space mapping maps the design parameters. Implicit space mapping takes advantage of the preassigned parameters which are not usually optimized to align the surrogate with the fine model. In this case the mapping is implicit. We also can apply output mapping to the response of the coarse model as a final touchup to the models that are not perfectly matched.

## Slide 8
Tuning Space Mapping (TSM): Type 0 and Type 1
(Cheng et al., 2012)
1
2
3
Notes: Explicit SM

## Slide 9
Tuning Space Mapping (TSM): Auxiliary Fine Model and Tuning Model (Cheng et al., 2012)
1. auxiliary fine model: fine model with tuning ports or split fine model components
2. tuning model: tuning components are added to the auxiliary fine model
 | Type 0– | Type 0 and 1 | Type 1d (fast) | Type 2
fine model |  |  |  | 
auxiliary fine model1 |  |  |  | 
tuning model2 |  |  |  | 
1
2
3
Notes: Explicit SM

## Slide 10
Tuning Space Mapping (TSM): Type 0 and Type 1 (Cheng et al., 2012) Type 0 tuning fine model auxiliary fine model conceptual tuning model Type 1 tuning fine model auxiliary fine model conceptual tuning model
1
2
3
1
2
3
Notes: Explicit SM

## Slide 11
Tuning Space Mapping (TSM): Type 1 and Type 1d (Cheng et al., 2012) Type 1 tuning
fine model auxiliary fine model conceptual tuning model Type 1d tuning fine model auxiliary fine model conceptual tuning model
1
2
3
1
2
3

## Slide 12
Tuning Space Mapping (TSM): Type 2 (Cheng et al., 2012) Type 2 tuning
fine model auxiliary fine model conceptual tuning model
1
2
3

## Slide 13
Tuning Space Mapping Optimization (Cheng et al., 2012)
the original optimization problem align tuning model with fine model optimize tuning model

## Slide 14
Tuning Space Mapping (TSM) Flowchart (Cheng et al., 2012)
1
2
3
Notes: Here is a flowchart showing you how the tuning space mapping works.
First of all, we select the coarse model and fine model for the problem, and a mapping process, such as input space mapping, aggressive space mapping, output space mapping, implicit space mapping, etc.
Then, we optimize the coarse model to obtain the initial guess of the fine model.
After that, we will simulate the fine model at the solution.
The first three steps are just what we did in the other space mapping methods.
After that, we should judge that if the specification of the optimization problem is satisfied.
If we have achieved the goal, the program terminated, if not, we should start iterative optimization and updating process on the tuning element.
In the first iteration, we should choose a suitable tuning element and add it at the tuning port in in the fine model.
In the other iterations, we will do optimization on the tuning element,
After that, a important step is to convert the tuning element into the fine model structure.
Since we get the corresponding fine model parameter, we can do the next fine model simulation.
The process will terminate when a stopping criterion is satisfied.

## Slide 15
Open-loop Ring Resonator Bandpass Filter (Koziel et al., 2008)
design parameters: x = [L1 L2 L3 L4 S1 S2 g]T mm
specifications: |S21|  −3 dB, 2.8-3.2 GHz |S21|  −20 dB, 1.5-2.5 GHz, 3.5-4.5 GHz
Notes: Explicit SM

## Slide 16
Open-loop Ring Resonator Bandpass Filter:
Types 1 and 0 Tuning Auxiliary Fine Model (Cheng et al., 2010) Sonnet em model with internal (co-calibrated) ports:
Notes: Explicit SM

## Slide 17
Open-loop Ring Resonator Bandpass Filter: Mixed Type 1 and Type 0 Tuning Model (Cheng et al., 2010) Sonnet em tuning model with tuning elements
(Type 0 elements in circles)
Notes: Explicit SM

## Slide 18
Open-loop Ring Resonator Bandpass Filter: Mixed Type 1 and Type 0 Tuning Model (Cheng et al., 2010)
initial responses: tuning model (—), fine model (○), fine model with co-calibrated ports (---)
|S21|
Notes: Explicit SM

## Slide 19
Open-loop Ring Resonator Bandpass Filter: Mixed Type 1 and Type 0 Tuning Model (Cheng et al., 2010)
responses after two iterations: the tuning model (—), corresponding fine model (○)
|S21|
Notes: Explicit SM

## Slide 20
Third-Order Chebyshev Filter (Kuo et al., 2003) fine model (Sonnet em) design variables: x = [L1 L2 S1 S2]T
design specifications: |S21|  –20 dB, 1.0-1.6 GHz, 2.4-3.0 GHz |S21|  –3 dB, 1.8-2.2 GHz

## Slide 21
Third-Order Chebyshev Filter: Type 1d (Fast) Tuning
(Koziel et al., 2010)
auxiliary fine model
tuning model
Notes: Explicit SM

## Slide 22
Third-Order Chebyshev Filter: Type 1d (Fast) Tuning
(Koziel et al., 2010)
initial fine model (),
tuning model (---), tuning model after the alignment procedure (…)
final model design (),
tuning model (---)
Notes: Explicit SM

## Slide 23
Coupled-line Bandpass Filter: Type 2 Tuning
(Koziel and Bandler, 2011)
conceptual tuning model tuning model
Notes: Explicit SM

## Slide 24
Coupled-line Bandpass Filter: Type 2 Tuning
(Koziel and Bandler, 2011)
final fine model responses obtained in two iterations
Notes: Explicit SM

## Slide 25
Conclusions
review of tuning techniques
categorize and illustrate tuning space mapping procedures
tuning space mapping is generally robust because of misalignment compensation by
physically valid tuning elements and
subsequent parameter extraction procedures
considerations: the engineer’s knowledge, available software, difficulties in implementation, simulation costs
our aim: to help engineers understand the methodology and to inspire new implementations and applications
Notes: Explicit SM

## Slide 26
References 1
J.W. Bandler, P.C. Liu, and H. Tromp, “A nonlinear programming approach to optimal design centering, tolerancing and tuning,” IEEE Trans. Circuits and Systems, vol. 23, no. 3, pp. 155-165, Mar. 1976.
J.W. Bandler, M.R.M. Rizk, and A.E. Salama, “An interactive optimal postproduction tuning technique utilizing simulated sensitivities and response measurements,” IEEE Int. Microwave Symp. Digest, Los Angeles, CA, June 1981, pp. 63-65.
J.W. Bandler and A.E. Salama, “Integrated approach to microwave postproduction tuning,” IEEE Int. Microwave Symp. Digest, Boston, MA, May-June 1983, pp. 415-417.
J.W. Bandler and A.E. Salama, “Functional approach to microwave postproduction tuning,” IEEE Trans. Microwave Theory Tech., vol. 33, no. 4, pp. 302-310, Apr. 1985.
J.W. Bandler, Q.S. Cheng, S.A. Dakroury, A.S. Mohamed, M.H. Bakr, K. Madsen, and J. Søndergaard, “Space mapping: the state of the art,” IEEE Trans. Microwave Theory Tech., vol. 52, no. 1, pp. 337-361, Jan. 2004.
Q.S. Cheng, J.W. Bandler, and J.E. Rayas-Sánchez, “Tuning-aided implicit space mapping,” Int. J. RF and Microwave CAE, vol. 18, no. 5, pp. 445-453, Sep. 2008.
Q.S. Cheng, J.W. Bandler, and S. Koziel, “Space mapping design framework exploiting tuning elements,” IEEE Trans. Microwave Theory Tech., vol. 58, no. 1, pp. 136-144, Jan. 2010.
Q.S. Cheng, J.W. Bandler, and S. Koziel, “Tuning space mapping: the state of the art,” Int. J. RF and Microwave CAE, 2012.
Notes: Explicit SM

## Slide 27
References 2
Q.S. Cheng, J.C. Rautio, J.W. Bandler, and S. Koziel, “Progress in simulator-based tuning—the art of tuning space mapping,” IEEE Microwave Magazine, vol. 11, no. 4, pp. 96-110, June 2010.
S. Koziel, J. Meng, J.W. Bandler, M.H. Bakr, and Q.S. Cheng, “Accelerated microwave design optimization with tuning space mapping,” IEEE Trans. Microwave Theory Tech., vol. 57, no. 2, pp. 383-394, Feb. 2009.
S. Koziel, J.W. Bandler, and Q.S. Cheng, “Design optimization of microwave circuits through fast embedded tuning space mapping,” Proc. 40th European Microwave Conf., Paris, France, Sep./Oct. 2010, pp. 1186-1189.
S. Koziel, J.W. Bandler, and Q.S. Cheng, “Tuning space mapping design framework exploiting reduced EM models,” IET Microwaves, Antennas & Propagation, vol. 5, no. 10, pp. 1219-1226, July 2011.
S. Koziel and J.W. Bandler, “Fast design optimization of microwave structures using co-simulation-based tuning space mapping,” Applied Computational Electromagnetics Society Journal, vol. 26, no. 8, pp. 631-639, Aug. 2011.
J.F. Pinel, “Computer-aided network tuning,” IEEE Trans. Circuit Theory, vol. 18, no. 1, pp. 192-194, Jan. 1971.
A. Rasmita, Y.X. Guo, and A. Alphones, “Constrained explicit knowledge embedded space mapping using circuit tuning based on physical augmentation as parameter extraction,” Asia Pacific Microwave Conf. (APMC), Dec. 2009, pp. 1431-1434.
P. Thoma, “Using coupled simulations to efficiently address challenging EM problems,” Int. Workshop on Advances in Modeling and Optimization of High Frequency Structures, Reykjavik University, Iceland, Aug. 21-22, 2010.
Notes: Explicit SM

## Slide 28
References 3
J.C. Rautio, “RF design closure—companion modeling and tuning methods,” IEEE Int. Microwave Symp. Workshop: Microwave component design using space mapping technology, San Francisco, CA, June 2006.
D. G. Swanson, Jr., and R. J. Wenzel, “Fast analysis and optimization of combline filters using FEM,” IEEE Int. Microwave Symp. Digest, 2001, pp. 1159-1162.
M. Yu and W.-C. Tang, “A fully automated filter tuning robot for wireless base station diplexers,” IEEE Int. Microwave Symp. Workshop on Computer Aided Filter Tuning, Philadelphia, PA, June 2003.
N. Zahirovic, R.R. Mansour, and M. Yu, “Scalar measurement-based algorithm for automated filter tuning of integrated Chebyshev tunable filters,” IEEE Trans. Microwave Theory Tech., vol. 58, no. 12, pp. 3749-3759, Dec. 2010.
Notes: Explicit SM